## Slide 1: Hierarchical Optimization Technique for Placement of Visual Landmarks for Robot Navigation in Repetitive Structured Indoor Environments
Abinaya S, Nivetha S, Kiruthik V,
Dr. Rakesh Kumar Sidharthan
Paper id: 48

## Slide 2: Agenda
Abstract
Introduction
Research gap and novelty of the work
Objectives
Methodology
Result
Conclusion

## Slide 3: Abstract
Autonomous indoor navigation poses significant challenges, particularly in visually repetitive GPS-denied environments, such as hotel corridors, hospital rooms, and shopping malls.
Visual markers like ArUco (Augmented Reality University of Córdoba) tags can serve as reliable navigation beacons by providing unique landmarks for robot localization. However, determining the optimal placement of these markers is crucial, as excessive placement creates visual clutter while insufficient placement makes reliable robot navigation challenging.
To overcome this problem, the proposed work aims to develop a hierarchical optimization technique that automates the placement of visual markers in the given environment, enabling autonomous navigation.
Three different types of markers, namely functional, junction, and corridor tags, are used to provide structural information to the robot. Mathematical feasibility analysis is carried out to select optimal marker parameters based on camera intrinsics and environmental constraints. Greedy search-based hierarchical placement logic is used to determine the optimal placement and density of markers.
Simulation study results in marker availability of 94.2%, while reducing the marker usage by 82% in structured environment. A reliable 100% marker availability is observed at junctions, where robot navigation is challenging. A mean visibility of 1.011 tags per frame is reported, thereby offering autonomous indoor navigation more accessible for real-world applications.

## Slide 4: Introduction
Indoor navigation remains a challenging problem due to the absence of GPS and the unreliability of wireless signals such as Wi-Fi, which are affected by interference and multipath effects. This makes accurate and consistent localization difficult, especially in structured indoor environments like corridors.
Structured indoor environments such as corridors often contain repetitive features, leading to ambiguity in visual localization.
To address this, visual markers such as ArUco tags can be used as navigation beacons, providing unique reference points for the robot. These markers are low-cost, easy to detect, and suitable for real-time application
However, the effectiveness of such systems strongly depends on how these markers are placed within the environment.

## Slide 5: Research gap and novelty
Existing approaches often rely on dense marker placement, leading to redundancy and increased cost.
Advanced optimization methods improve placement quality but require detailed modeling and are less practical for structured indoor environments
Limited focus on visibility constraints and robot-specific perception instructured indoor environments. Lack of a practical, scalable approach for efficient marker placement
A visibility-aware marker placement strategy considering robot field of view and environment structure
Hierarchical placement prioritizing critical areas such as junctions and functional points
Use of greedy optimization within a structured, environment-aware framework
A practical and scalable alternative to computationally intensive optimization methods

## Slide 6: Objectives
To Calibrate of the onboard camera system to determine the size and ensure accurate ArUco markers.
To Configure of functionally specific markers and feasibility analysis for marker placement.
To Design of a hierarchical optimization technique for the placement of ArUco markers by analyzing spatial constraints, visibility requirements, and navigation performance.
To Validate of the proposed technique using simulation and in a real-time environment.

## Slide 7: Methodology

## Slide 8: Methodology - Environment definition
A hotel-like indoor corridor environment characterized by repetitive structures is designed for the proposed study
The environment includes functional areas such as doors and junctions, which are prone to localization errors.
Corridor width is measured to define lateral visibility and the required bearing angles for detecting junctions before and after turns.
The beacons are categorized into three types based on placement locations as follows:
Functional Tags(F) – placed at doors or task areas
Junction Tags(J) – placed at intersections
Corridor Tags(C) – for straight-line navigation.
Structured, repetitive test environment

## Slide 9
The algorithm is deployed using MATLAB, and the results obtained are validated with Webots simulation software and real-world testing using physical hardware over evaluation metrics which includes
Localization availability,
Placement efficiency,
Blackout regions,
Junction availability, and
Redundancy
Structured repetitive environment
Simulation environment
Real-world environment
Environment in MATLAB
Methodology - Environment definition

## Slide 10: Methodology - Manual placement
Methodology for optimizing tag placement in a robot's workspace to maximize localization availability across different corridor configurations
Single-sided
Alternative
Random

## Slide 11: Manual placement – Setup
Non optimal uniform placement - Tags are placed manually at a uniform distance of 25cm for both single and alternate wall.
Optimal placement – Tags are placed following the visibility constraints of maximum detection distance, and maximum Horizontal field of view obtained from camera parameters
Efficiency of tag placement by comparing mean visible tags per frame against localization availability
Graph comparing visibility and a line plot tracking the number of visible tags over distance
Case | Availability | Junction Avail | Redundancy
Opt C1 | 75 | 56.25 | 11.11
Opt C2 | 86.11 | 68.75 | 13.88
Opt C3 | 88.88 | 75 | 11.11
Non-Opt C1 | 77.77 | 68.75 | 44.44
Non-Opt C2 | 77.77 | 68.75 | 30.55

## Slide 12: Methodology – Inferences from manual placement
Placement Strategy
Uniform placement leads to high redundancy (>40%), improving robustness but also increasing cost and complexity
Strategic placement reduces redundancy while maintaining reliability
Alternating placement is effective for wide corridors
Single-side placement is sufficient for narrow corridors
Marker Design​
Very small tags reduce localization accuracy due to poor detection ​
Oversized tags overcrowd the camera field of view, reducing efficiency ​
Optimal tag size must balance detectability and field-of-view coverage​
Critical Locations
Marker placement at junctions and functional points is essential for reliable navigation
Pre- and post-junction markers improve re-localization and reduce navigation failures

## Slide 13: Methodology - Hierarchical Optimization Framework
A hierarchical multi-stage optimization algorithm is designed to optimize the placement and number of ArUco tags to ensure reliable indoor robot navigation with minimal infrastructure.
Minimal infrastructure refers to the trade-off between reduction of Aruco tags while increasing the localization availability.
Flow chart of the proposed hierarchical optimization technique for visual landmark placement

## Slide 14
The objective is to select a minimal subset of ArUco tags S from a candidate pool C, such that the robot’s path P achieves maximum localization availability
Feasibility analysis - The following are the constraints used
Detection feasibility
A tag is only selected if its distance d satisfies as shown in eq
Geometric visibility
The bearing angle relative to the robot must satisfy the​
constraint described in eq
Mandatory placement
Functional and junction tags to be selected, as shown
in condition eq
Hierarchical Optimization Framework – Feasibility analysis

## Slide 15: Feasibility Analysis -
The pixel threshold increases as the maximum detection distance decreases for ArUco tags. Hence, ArUco markers of different sizes (0.10m, 0.15m, and 0.20 m) are evaluated
Tag_m | PxThr | MaxDist_m
0.1 | 30 | 0.73
0.1 | 40 | 0.55
0.1 | 50 | 0.44
0.15 | 30 | 1.1
0.15 | 40 | 0.82
0.15 | 50 | 0.66
0.2 | 30 | 1.46
0.2 | 40 | 1.1
0.2 | 50 | 0.88
As the pixel threshold increases, the maximum detection distance decreases for ArUco tags of different sizes (0.10 m, 0.15 m, and 0.20 m).
The proposed feasibility analysis technique selects an optimal configuration of 0.2m tags with a 40px threshold, providing a maximum detection distance (dmax) of 1.1m.
Possible candidates for placement

## Slide 16
Hierarchical Optimization Framework – Visibility matrix
The algorithm utilizes camera intrinsics (fx, fy) and pixel thresholds (PxThr) to calculate the maximum detection distance (dmax), as shown in eq.
A visibility matrix(V) is derived by sampling potential robot poses along the centerline of the robot path and evaluated for distance, bearing angle and occlusion constraints.
1. Lateral visibility: Dmax must exceed the maximum wall offset to ensure the robot can visualize the side walls from the corridor centerline
2. Corridor coverage: Dmax must exceed the maximum corridor width to ensure continuous coverage.

## Slide 17: Visibility matrix
Candidate tags (Cj) are generated along all wall surfaces with a uniform spacing, enabling the set of tags to satisfy the visibility constraints
It is described as binary visibility state for every given robot pose (Pi)

## Slide 18
Hierarchical Optimization Framework – Multi-Stage Tag Placement
Stage 1 - Functional Tags
The algorithm initially prioritizes high-priority task areas. Candidate tags that are closest to the doorways are selected to ensure task-specific localization.
Stage 2 - Junction Tags
Tags are selected for placement at junctions in the corridor, where pre-turn and post-turn of robot leads to localization errors and reliable markers are re- quired. In our work, L- and T- based intersections are considered as junctions​
​
Stage 3 - Corridor Tags
The remaining straight corridors are filled using a greedy iterative algorithm that selects tags from the candidate pool based on a weighted objective function.
Score = New Coverage − Penalty

## Slide 19: Results– Iterative Optimization
Iter | Coverage (%) | 0 tags Covered | Candidates | Total Tags
1 | 64.49 | 49 | 158 | 21
2 | 68.84 | 43 | 157 | 22
3 | 73.19 | 37 | 156 | 23
4 | 77.54 | 31 | 155 | 24
5 | 81.88 | 25 | 154 | 25
6 | 84.78 | 21 | 153 | 26
7 | 86.96 | 18 | 152 | 27
8 | 89.13 | 15 | 151 | 28
9 | 90.58 | 13 | 150 | 29
10 | 92.03 | 11 | 149 | 30
11 | 93.48 | 9 | 148 | 31
12 | 94.20 | 8 | 147 | 32
The straight corridor stage minimizes coverage gaps and maximizes overall localization availability while strategically placing tags to eliminate redundancy and lower infrastructure costs.
The iterative greedy optimization loop, dynamically selects the candidate tag that maximizes new pose coverage at each step, penalizing close-range placements on the same wall.​
​

## Slide 20: Result –Evaluation report generated
Stage | Tags Used(%) | No.Tags Used | Total Candidates | Reduction(%) | Localization Availability(%) | Total Blackout Length(m)
Functional Tags | 2.2 | 4 | 178 | 97.8 | 21.7 | 4.9
Junction Tags | 11.2 | 20 | 178 | 88.8 | 60.1 | 2.3
Straight | 18 | 32 | 178 | 82 | 94.2 | 0.3

## Slide 21: Result –Validation in the Simulation environment
The results obtained from the algorithm that was deployed in MATLAB is validated and tested in the simulation environment with the same environment and Evaluation metrics to check the reliability of the algorithm.
Metric | Value
Total Distance Travelled | 13.73 m
Mean Tags Visible | 1.011
Max Tags Observed | 3
Localization Reliability (Path with ≥ 1 Tag) | 94.58%
Blackout Rate (Failure) (Path with 0 Tags) | 6.32%
Redundancy Rate (Optimal) (Path with ≥ 2 Tags) | 8.21%

## Slide 22: Hardware Utilized
Jetbot
Sensor: Sony IMX219
Resolution: 8 Megapixels (3280 x 2464 pixels).
Focal Length: 3.15 mm
Field of View (FOV): 160° ultra-wide angle.

## Slide 23: Result - Validation in Real world Environment
The robots are operated with three different speed type and the results are observed.
Speed types:
•slow speed – 5.54cm/s
•medium speed - 8.71cm/s
•high speed – 15.24cm/s
Metric | Value
Total Frames | 2666
Blackout Percentage | 8.18%
Availability Percentage | 91.82%
Redundancy | 8.21%

## Slide 24: Conclusion
Visual landmarks like ArUco markers provide reliable beacons for robot navigation in a structurally repetitive indoor environment. A hierarchical three-stage optimization algorithm is proposed to place the ArUco markers, enabling robot navigation. Inference generated from the manual placement provides insight into tag placement.
Visibility awareness and structure-specific deployment of tags are considered in this study. A greedy search algorithm is used to optimize the tag placement.
Experimental analysis results in 94.2 % of tag availability. Validation in the simulation and real-world environment also results in a mean visibility of 1.011 tags per frame.
Development of an end-to-end automated strategy for automated marker placement using machine learning techniques will be the extension of the pro- posed work.
Integration of sensor fusion techniques to combine visual markers information with IMU and wheel odometry will be investigated in the future.

## Slide 25: References
R. A. Deshmukh et al., “Advancing indoor positioning systems: innovations, chal lenges, and applications in mobile robotics,” Robotica, vol. 43, no. 7, pp. 2710–2750, 2025. doi:10.1017/S0263574725101872.
Abdulla, A.A., Liu, H., Stoll, N., Thurow, K.: A backbone-floyd hybrid path plan ning method for mobile robot transportation in multi-floor life science laboratories. In: 2016 IEEE International Conference on Multisensor Fusion and Integration for Intelligent Systems (MFI), pp. 406–411. IEEE, Baden-Baden (2016)
Huang, J., Junginger, S., Liu, H., Thurow, K.: Indoor positioning systems of mobile robots: A review. Robotics 12(2), 47 (2023)
Vincent, R., Limketkai, B., Eriksen, M.: Comparison of indoor robot localization techniques in the absence of GPS. In: Detection and Sensing of Mines, Explosive Objects, and Obscured Targets XV, vol. 7664, pp. 606–610. SPIE, Orlando (2010)
Bach, S.H., Khoi, P.B., Yi, S.Y.: Application of QR code for localization and navi gation of indoor mobile robot. IEEE Access 11, 28384–28390 (2023)
Pandey, S., Verma, C., Trivedi, E., Mehendale, N.: AprilTag-Based Self Localization for Drones in Indoor Environments. SSRN Electronic Journal (2024). https://doi.org/10.2139/ssrn.4815151
Patrioli, L.: Development of a localization system based on aruco markers for a small space platforms test bench. Doctoral dissertation, Politecnico di Torino (2020)
Vijay, C.S., Megalingam, R.K.: Autonomous Navigation of Lab Assisting Mobile Robot Using SLAM. In: 19th India Council International Conference (INDICON), pp. 1–6. IEEE, Kochi (2022)
Sarwar, M.M.S., Yadav, R., Samanta, S., Ray, R., Halder, R., Banda, G.: A Robotic Software Framework for Autonomous Navigation in Unknown Environment. In: In ternational Symposium of Asian Control Association on Intelligent Robotics and Industrial Automation (IRIA), pp. 1–6. IEEE, Goa (2021)

## Slide 26: References
Alghamdi, M., Al-Marakeby, A., Abdel-Mageid, S.: Mobile Robot Navigation Based on Artificial Markers: A Systematic Mapping Study. Journal of Robotics and Mechatronics 37(3), 762–778 (2025)
.Megalingam, R.K., Madhuri, S.L., Santhoshini, T., Juluri, V.: Robot Navigation Through QR and Text Detection. In: Smys, S., Palanisamy, R., Rocha, ´ A., Beligian nis, G.N. (eds.) Computer Networks and Inventive Communication Technologies, vol. 58, pp. 197–208. Springer, Singapore (2021)
Mantha, B.R.K., Garc´ıa de Soto, B.: Investigating the Fiducial Marker Network Characteristics for Autonomous Mobile Indoor Robot Navigation Using ROS and Gazebo. Journal of Construction Engineering and Management 148(10), 1–15 (2022)
Beinhofer, M., M¨uller, J., Krause, A., Burgard, W.: Robust Landmark Selection for Mobile Robot Navigation. In: IEEE/RSJ International Conference on Intelligent Robots and Systems, pp. 1–7. IEEE, Tokyo (2013)
Hinderer, S., Scheffler, M., Yang, B.: Investigation of ArUco Marker Placement for Planar Indoor Localization. arXiv preprint arXiv:2509.17345 (2025)
Basso, G.: Improved Pose Estimation of ArUco Tags Using a Novel 3D Placement Strategy. Sensors 20(17), 4825 (2020)
Kayhani, N., Schoellig, A., McCabe, B.: Perception-Aware Tag Placement Planning for Robust Localization of UAVs in Indoor Environments. Journal of Computing in Civil Engineering 37(2), 1–14 (2023)
Krishna, S., Rahul, E.S., Bhavani, R.R.: RFID based human localization in robot cells for a better shared workspace interaction. CSI Transactions on ICT 4(1), 37–43 (2016)

## Slide 27
Thank You